## Slide 1: Sequential Execution Semantics
Contract: How the machine appears to behave

## Slide 2: Sequential Semantics - Review
Instructions appear as if they executed:
  In “program order”
    As if they executed one after the other
Program
Order
Pipelining
Superscalar
Out-of-Order

## Slide 3: Execution Order?
addi r2, r1, 10
addi r3, r2, 20
add r5, r4, 30
add r6, r5, 40

## Slide 4: Execution Order? Dependencies
addi r2, r1, 10
addi r3, r2, 20
add r5, r4, 30
add r6, r5, 40

## Slide 5: Execution Order? Pipelined and Superscalar
addi r2, r1, 10
addi r3, r2, 20
add r5, r4, 30
add r6, r5, 40
addi r2, r1, 10
addi r3, r2, 20
add r5, r4, 30
add r6, r5, 40
Pipelining
Superscalar

## Slide 6: Execution Order? Out-of-Order
Superscalar
addi r2, r1, 10
addi r3, r2, 20
add r5, r4, 30
add r6, r5, 40
Out-of-Order
addi r2, r1, 10
addi r3, r2, 20
add r5, r4, 30
add r6, r5, 40

## Slide 7: Out-of-Order Execution
fetch
decode
fetch
decode
sub
bne
fetch
decode
add
fetch
decode
ld
fetch
decode
add
do {
sum += a[++m];
i--;
} while (i != 0);
out-of-order
loop: add r4, r4, 1
ld r2, 10(r4)
add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
fetch
decode
fetch
decode
sub
bne
fetch
decode
add
fetch
decode
ld
fetch
decode
add
Superscalar

## Slide 8: Sequential Semantics?
fetch
decode
fetch
decode
sub
bne
fetch
decode
add
fetch
decode
ld
fetch
decode
add
Execution does NOT adhere to sequential semantics
To be precise: Eventually it may
Simplest solution:
  Define problem away
  IBM 360 did this
Not acceptable today: e.g., Virtual Memory
Three-phase Instruction execution
  In-Progress, Completed and Committed
inconsistent
consistent

## Slide 9: Sequential Semantics?
Fetch I4
decode
Fetch I5
decode
sub
bne
Fetch I1
decode
add
Fetch I2
decode
ld
Fetch I3
decode
add
inconsistent
consistent
empty
Reorder buffer
Program order
empty
empty
empty
empty
Retire
Enter
empty

## Slide 10: Sequential Semantics?
Fetch I4
decode
Fetch I5
decode
sub
bne
Fetch I1
decode
add
Fetch I2
decode
ld
Fetch I3
decode
add
inconsistent
consistent
I1 F
Reorder buffer
Program order
I2 F
I3 F
I4 F
I5 F
Retire
Enter
empty

## Slide 11: Sequential Semantics?
Fetch I4
decode
Fetch I5
decode
sub
bne
Fetch I1
decode
add
Fetch I2
decode
ld
Fetch I3
decode
add
inconsistent
consistent
I1 D
Reorder buffer
Program order
I2 D
I3 D
I4 D
I5 D
Retire
Enter
empty
(destReg, old value)

## Slide 12: Sequential Semantics?
Fetch I4
decode
Fetch I5
decode
sub
bne
Fetch I1
decode
add
Fetch I2
decode
ld
Fetch I3
decode
add
inconsistent
consistent
I1 c
Reorder buffer
Program order
I2 D
I3 D
I4 c
I5 D
Retire
Enter
empty
completed

## Slide 13: Sequential Semantics?
I4 c
Fetch I4
decode
Fetch I5
decode
sub
bne
Fetch I1
decode
add
Fetch I2
decode
ld
Fetch I3
decode
add
inconsistent
consistent
empty
Reorder buffer
Program order
I2 c
I3 D
I5 c
Retire
Enter
empty
completed
committed

## Slide 14: Sequential Semantics?
Fetch I4
decode
Fetch I5
decode
sub
bne
Fetch I1
decode
add
Fetch I2
decode
ld
Fetch I3
decode
add
inconsistent
consistent
empty
Reorder buffer
Program order
empty
empty
I4 c
I5 c
Retire
Enter
empty
committed
completed

## Slide 15: Sequential Semantics?
Fetch I4
decode
Fetch I5
decode
sub
bne
Fetch I1
decode
add
Fetch I2
decode
ld
Fetch I3
decode
add
inconsistent
consistent
empty
Reorder buffer
Program order
empty
empty
empty
empty
Retire
Enter
empty

## Slide 16: Sequential Semantics?
Fetch I4
decode
Fetch I5
decode
sub
bne
Fetch I1
decode
add
Fetch I2
decode
ld
Fetch I3
decode
add
inconsistent
consistent
empty
Reorder buffer
Program order
I2 c
I3 D
I4 c
I5 c
Retire
Enter
empty
completed
committed
WHAT IF SOMEONE STOPS US HERE?

## Slide 17: Sequential Semantics?
empty
I2 c
I3 D
I4 c
I5 c
empty
Fetch I4
decode
Fetch I5
decode
sub
bne
Fetch I1
decode
add
Fetch I2
decode
ld
Fetch I3
decode
add
consistent
Reorder buffer
Program order
Retire
Enter
Undo changes
empty
Reorder buffer
Program order
empty
empty
empty
empty
Retire
Enter
empty

## Slide 18: Preserving Sequential Semantics: Three phases
Instr. exec. in 3 phases:
  In-progress, Completed, Committed
  OOO for in-progress and Completed
  In-order Commits
Completed - out-of-order: ”Visible only inside”
  Results visible to subsequent instructions
  Results not visible to outsiders
    On interrupts completed results are discarded
Committed - in-order: ”Visible to all”
  Results visible to subsequent instructions
  Results visible to outsiders
    On interrupt committed results are preserved

## Slide 19: Commit vs. Complete
Time
DIV R3, _, _
ADD R1, _, _
ADD _, R1, _
In-order
commits
in-order
completes
out-of-order completes
in-order commits
complete
fetch
decode
fetch
decode
sub
bne
fetch
decode
add
fetch
decode
ld
fetch
decode
add
commit
commit
commit
commit
commit

## Slide 20: Implementing Completes/Commits
Key idea:
  Maintain sufficient state around to be able to roll-back when necessary
  Roll-back:
    Discard (aka Squash) all not committed
One solution (conceptual): History File
  Upon Complete instruction records previous value of target register
  Upon Discard, instruction restores target value
  Upon Commit, nothing to do
Focus on scheduling mechanisms

## Slide 21: Solution #2: Future File
Two states:
  Architectural
    Updated only on commit
  Speculative
    Updated on complete
Normally use Speculative
On exception:
  Flush Speculative
  Use Architectural
Implementing precise interrupts in pipelined processors
J. E. Smith and A. Pleszkun,
http://www.eecg.toronto.edu/~moshovos/ACA07/readings/smith-interrupts.pdf

## Slide 22: Out-of-Order Execution Overview
Program Form
Processing Phase
Static program
dynamic inst.
Stream (trace)
execution
window
completed
instructions
Dispatch/ dependences
inst. Issue
inst execution
inst. Reorder &
commit
In-Progress
Completed
Committed

## Slide 23: Out-Of-Order Exec. Example
loop: add r4, r4, 4
ld r2, 10(r4) 4 cycles lat
add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
op
src1
src2
tgt
status
Reservation station

## Slide 24: Out-Of-Order Exec. Example
loop: add r4, r4, 4
ld r2, 10(r4) 4 cycles lat
add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
1
1
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
status
Register Availability Vector
AKA
Scoreboard

## Slide 25: Out-Of-Order Exec. Example
loop: add r4, r4, 4
ld r2, 10(r4) 4 cycles lat
add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
1
1
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
Cycle 0
status

## Slide 26
Out-Of-Order Exec. Example: Cycle 0
1
1
1
0
r1
r2
r3
r4
RAV
op
src1
src2
tgt
Cycle 0
add
r4/1
NA/1
r4/0
Rdy
status
loop: add r4, r4, 4
ld r2, 10(r4)
add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
Ready to be
executed

## Slide 27
Cycle 1
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
0
1
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Exec
status
ld
r4/1
NA/1
r2
Rdy
R4 gets produced now
Notify those waiting for R4

## Slide 28
Cycle 2
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
0
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
add
r3/1
r2/0
r3
Wait

## Slide 29
Cycle 3
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
0
0
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
add
r3/1
r2/0
r3
Wait
sub
r1/1
NA/1
r1
Rdy
No dependences

## Slide 30
Cycle 4
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
0
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
add
r3/1
r2/0
r3
Wait
sub
r1/1
NA/1
r1
Exec
r1 produced now
Notify consumers
bne
r1/1
r0/1
NA
Rdy
r1 will be available next cycle

## Slide 31
Cycle 5
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
0
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
add
r3/1
r2/0
r3
Wait
sub
r1/1
NA/1
r1
Compl
Completed
bne
r1/1
r0/1
NA
Exec
executing

## Slide 32
Cycle 6
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
1
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
Notify consumers
add
r3/1
r2/1
r3
Rdy
sub
r1/1
NA/1
r1
Compl
Completed
bne
r1/1
r0/1
NA
Exec
executing

## Slide 33
Cycle 7
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
1
1
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Cmtd
Executing
Notify consumers
add
r3/1
r2/1
r3
Exec
sub
r1/1
NA/1
r1
Compl
Completed
bne
r1/1
r0/1
NA
Compl

## Slide 34
Cycle 8
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
1
1
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Cmtd
add
r3/1
r2/1
r3
Cmtd
sub
r1/1
NA/1
r1
Cmtd
bne
r1/1
r0/1
NA
Cmtd

## Slide 35: Window vs. Scheduler
Window
  Distance between oldest and youngest instruction that can co-exist inside the CPU
  Larger window  Potential for more ILP
Scheduler
  Number of instructions that are waiting to be issued
Window
  Instructions enter at Fetch
  Exit at Commit
Scheduler
  Instructions enter at Decode
  Leave at writeback/complete
Window >= Scheduler
  Can be the same structure
In window but not in scheduler  completed
instructions

## Slide 36: Speculative Execution
Why?
  1 every 5 insts is a branch (control flow)
  Today’s processors have a window of 128 insts
  Can’t wait until a branch is resolved to fetch next set of insts
  Solution: Speculate
Fetch branch
Resolve branch
Wrong
squash

## Slide 37: Beyond Simple OoO
A
B
C
D
E
A: LF F6, 34(R2)
B: LF F2, 45(R3)
C: MULF F0, F2, F4
D: SUBF F8, F2, F6
E: ADDF F2, F7, F4
E will wait for B, C and D.
WAR w/ C and D
WAW w/ B
Can we do better?

## Slide 38: What if we had infinite registers
A: LF F6, 34(R2)
B: LF F2, 45(R3)
C: MULF F0, F2, F4
D: SUBF F8, F2, F6
E: ADDF F2, F7, F4
A: LF F6, 34(R2)
B: LF F2, 45(R3)
C: MULF F0, F2, F4
D: SUBF F8, F2, F6
E: ADDF F9, F7, F4
No false dependences anymore
Since we do not reuse a name we can’t have WAW and WAR

## Slide 39: Register Renaming
Register Version
  Every Write creates a new version
  Uses read the last version
  Need to keep a version until all uses have read it.
Register Renaming:
  Architectural vs. Physical Registers
    more phys. than arch.
  Maintain a map of arch. to phys. regs.
  Use in-order decoding to properly identify dependences.
  Instructions wait only for input op. availability.
  Only last version is written to reg. file.

## Slide 40: Register renaming example
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p3
p4
p5
p5
p1

## Slide 41: Register renaming example
First rename input operands:
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p3
p4
p5
p5
p1

## Slide 42: Register renaming example
Then rename destination
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p3
p4
p5
p5
p4
From free list
r1
p1
ROB
For recovery purposes

## Slide 43: Register renaming example
Rename inputs
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p3
p4
p5
p5
p4
From free list
r1
p1
ROB
For recovery purposes

## Slide 44: Register renaming example
Rename destination
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p5
p4
p5
p5
p4
From free list
r1
p1
ROB
For recovery purposes
r3
p3

## Slide 45: Bird’s Eye View of a Modern CPU
Execution
Dispatch
Decode & Rename
Fetch
I Cache
Reorder Buffer
Execution Units
D Cache
In order retirement
Misspeculation handling