## Slide 1: Independence Instruction Set Architectures
Conventional ISA
  Instructions execute in order
No way of stating
  Instruction A is independent of B
    Must detect at runtime  cost: time, power, complexity
Idea:
  Change Execution Model at the ISA model
  Allow specification of independence
VLIW Goals:
  Flexible enough
  Match well technology
Vectors and SIMD
  Only for a set of the same operation

## Slide 2: VLIW
Very Long Instruction Word
#1 defining attribute
  The four instructions are independent
Some parallelism can be expressed this way
Extending the ability to specify parallelism
  Take into consideration technology
  Recall, delay slots
  This leads to 
#2 defining attribute: NUAL
  Non-unit assumed latency
ALU1
ALU2
MEM1
control
Instruction format

## Slide 3: NUAL vs. UAL
Unit Assumed Latency (UAL)
  Semantics of the program are that each instruction is completed before the next one is issued
  This is the conventional sequential model
Non-Unit Assumed Latency (NUAL):
  At least 1 operation has a non-unit assumed latency, L, which is greater than 1
  The semantics of the program are correctly understood if exactly the next L-1 instructions are understood to have issued before this operation completes
NUAL: Result observation is delayed by L cycles

## Slide 4: #2 Defining Attribute: NUAL
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
Assumed latencies for all operations
visible
visible
visible
visible
Glorified delay slots
Additional opportunities for specifying parallelism

## Slide 5: #3 DF: Resource Assignment
The VLIW also implies allocation of resources
The spec. inst format maps well onto the following datapath:
ALU1
ALU2
MEM1
control
ALU
ALU
cache
Control
Flow
Unit

## Slide 6: VLIW: Definition
Multiple independent Functional Units
Instruction consists of multiple independent instructions
Each of them is aligned to a functional unit
Latencies are fixed
  Architecturally visible
Compiler packs instructions into a VLIW also schedules all hardware resources
Entire VLIW issues as a single unit
Result: ILP with simple hardware
  compact, fast hardware control
  fast clock
  At least, this is the goal

## Slide 7: VLIW Example
I-fetch &
Issue
FU
FU
Memory
Port
Memory
Port
Multi-ported
Register
File

## Slide 8: VLIW Example
ALU1
ALU2
MEM1
control
Instruction format
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
Program order and execution order
Instructions in a VLIW are independent
Latencies are fixed in the architecture spec.
Hardware does not check anything
Software has to schedule so that all works

## Slide 9: Compilers are King
VLIW philosophy:
  “dumb” hardware
  “intelligent” compiler
Key technologies
  Predicated Execution
  Trace Scheduling
    If-Conversion
  Software Pipelining

## Slide 10: Predicated Execution
Instructions are predicated
  if (cond) then perform instruction
  In practice
    calculate result
    if (cond) destination = result
Converts control flow dependences to data dependences
if ( a == 0)
  b = 1;
  else b = 2;
true; pred = (a == 0)
pred; b = 1
!pred; b = 2

## Slide 11: Predicated Execution: Trade-offs
Is predicated execution always a win?
Is predication meaningful for VLIW only?

## Slide 12: Trace Scheduling
Goal:
  Create a large continuous piece or code
  Schedule to the max: exploit parallelism
“Fact” of life:
  Basic blocks are small
  Scheduling across BBs is difficult
But:
  While many control flow paths exist
  There are few “hot” ones

## Slide 13: Trace Scheduling
Trace Scheduling
  Static control speculation
  Assume specific path
  Schedule accordingly
  Introduce check and repair code where necessary
First used to compact microcode
  FISHER, J. Trace scheduling: A technique for global microcode compaction. IEEE Transactions on Computers C-30, 7 (July 1981), 478--490.

## Slide 14: Trace Scheduling: Example
Expand the scope/flexibility of code motion
A
B
C
A
C
Assume AC is the common path
A&C
schedule
Repair
B

## Slide 15: Trace Scheduling: Example #2
bA
bB
bC
bD
bE
bA
bB
bC
bD
check
all OK
repair
bC
bD
repair
bE

## Slide 16: Trace Scheduling Example
test = a[i] + 20;
If (test > 0) then
  sum = sum + 10
else
  sum = sum + c[i]
c[x] = c[y] + 10
test = a[i] + 20
sum = sum + 10
c[x] = c[y] + 10
if (test <= 0) then goto repair
…
Straight code
assume delay
repair:
sum = sum – 10
sum = sum + c[i]

## Slide 17: SIMD
Single Instruction Multiple Data

## Slide 18: SIMD: Motivation Contd.
Recall:
  Part of architecture is understanding application needs
Many Apps:
  for i = 0 to infinity
    a(i) = b(i) + c
Same operation over many tuples of data
Mostly independent across iterations

## Slide 19: Some things are naturally parallel

## Slide 20: Sequential Execution Model / SISD
int a[N]; // N is large
for (i =0; i < N; i++)
  a[i] = a[i] * fade;
time
Flow of control / Thread
One instruction at the time
Optimizations possible at the machine level

## Slide 21: Data Parallel Execution Model / SIMD
int a[N]; // N is large
for all elements do in parallel
  a[i] = a[i] * fade;
time
This has been tried before: ILLIAC III, UIUC, 1966
http://ieeexplore.ieee.org/xpls/abs_all.jsp?arnumber=4038028&tag=1
http://ed-thelen.org/comp-hist/vs-illiac-iv.html

## Slide 22: SIMD Processing
+
r1
r2
r3
add r3, r1, r2
SCALAR
(1 operation)
add r3, r1, r2
SIMD
(N operations)
+
r1
r2
r3
+
r1
r2
r3
+
r1
r2
r3
+
r1
r2
r3
+
r1
r2
r3

## Slide 23
TIME
fetch
decode
rf
exec
wb
C1
C2
C3
C4
C5
C6
C7
C8
C9
C10
exec
exec
wb
wb
fetch
decode
rf
exec
wb
exec
exec
wb
wb

## Slide 24
TIME
fetch
decode
rf
exec
wb
C1
C2
C3
C4
C5
C6
C7
C8
C9
C10
exec
exec
wb
wb
fetch
decode
rf
exec
wb
exec
exec
wb
wb
fetch
decode
rf
exec
wb
exec
exec
wb
wb

## Slide 25: SIMD Architecture
Replicate Datapath, not the control
All PEs work in tandem
CU orchestrates operations
CU
PE
MEM
PE
MEM
PE
MEM
ALU
μCU
regs

## Slide 26: Multimedia extensions
SIMD in modern CPUs

## Slide 27: MMX: Basics
Multimedia applications are becoming popular
Are current ISAs a good match for them?
Methodology:
  Consider a number of “typical” applications
  Can we do better?
  Cost vs. performance vs. utility tradeoffs
Net Result: Intel’s MMX
Can also be viewed as an attempt to maintain market share
  If people are going to use these kind of applications we better support them

## Slide 28: Multimedia Applications
Most multimedia apps have lots of parallelism:
  for I = here to infinity
    out[I] = in_a[I] * in_b[I]
  At runtime:
    out[0] = in_a[0] * in_b[0]
    out[1] = in_a[1] * in_b[1]
    out[2] = in_a[2] * in_b[2]
    out[3] = in_a[3] * in_b[3]
    …..
Also, work on short integers:
  in_a[i] is 0 to 256 for example (color)
  or, 0 to 64k (16-bit audio)

## Slide 29: Observations
32-bit registers are wasted
  only using part of them and we know
  ALUs underutilized and we know
Instruction specification is inefficient
  even though we know that a lot of the same operations will be performed still we have to specify each of the individually
  Instruction bandwidth
  Discovering Parallelism
  Memory Ports?
    Could read four elements of an array with one 32-bit load
    Same for stores
    The hardware will have a hard time discovering this
      Coalescing and dependences

## Slide 30: MMX Contd.
Can do better than traditional ISA
  new data types
  new instructions
Pack data in 64-bit words
  bytes
  “words” (16 bits)
  “double words” (32 bits)
Operate on packed data like short vectors
  SIMD
  First used in Livermore S-1 (> 20 years)

## Slide 31: MMX:Example
Up to 8 operations (64bit) go in parallel
Potential improvement: 8x
In practice less but still good
Besides another reason to think your machine
is obsolete

## Slide 32: Data Types

## Slide 35: Vector Processors
Scalar processors operate on single numbers (scalars)
Vector processors operate on vectors of numbers
  Linear sequences of numbers
+
r1
r2
r3
add r3, r1, r2
SCALAR
(1 operation)
v1
v2
v3
+
vector
length
vadd.vv v3, v1, v2
VECTOR
(N operations)
From. Christos Kozyrakis, Stanford

## Slide 36
TIME
fetch
decode
rf
exec
wb
C1
C2
C3
C4
C5
C6
C7
C8
C9
C10
exec
exec
wb
wb
rf
rf
fetch
decode
rf
exec
wb
exec
exec
wb
wb
rf
rf
fetch
decode
rf
exec
wb
exec
exec
wb
wb
rf
rf

## Slide 37: Example of Simple Vector Processor

## Slide 38: What’s in a Vector Processor
A scalar processor (e.g. a MIPS processor)
  Scalar register file (32 registers)
  Scalar functional units (arithmetic, load/store, etc)
A vector register file (a 2D register array)
  Each register is an array of elements
    E.g. 32 registers with 32 64-bit elements per register
  MVL = maximum vector length = max # of elements per register
A set for vector functional units
  Integer, FP, load/store, etc
  Some times vector and scalar units are combined (share ALUs)

## Slide 39: Vector Code Example
Y[0:63] = Y[0:63] + a * X[0:63]
LD R0, a
VLD V1, 0(Rx) V1 = X[]
VLD V2, 0(Ry) V2 = Y[]
VMUL.SV V3, R0, V1 V3 = X[]*a
VADD.VV V4, V2, V3 V4 = Y[]+V3
VST V4, 0(Ry) store in Y[]